## Slide 1
Air Gap Shape Optimization for Minimizing Proximity Effect Losses in an Inductor
, , ,
[1] Schneider Electric, Global Technology Eybens, France
[2] Univ. Grenoble Alpes, CNRS, Grenoble INP, G2ELab, F-38000, Grenoble, France
[3] Univ. Grenoble Alpes, CNRS, Grenoble INP, LJK, 38000 Grenoble, France
[4] Electrical Engineering Department, ENS Paris-Saclay, Université Paris-Saclay, 91190 Gif-sur-Yvette, France
[5] Université Paris-Saclay, CentraleSupélec, Sorbonne Université, CNRS, GeePs, 91192 Gif-sur-Yvette, France
[6] Johann Radon Institute for Computational and Applied Mathematics (RICAM), ÖAW, 4040 Linz, Austria
1

## Slide 2: Introduction
We want to optimize an inductor to minimize the AC losses due to the fringing effect.
Possible solutions :
Distributed air gaps
Change winding distribution of the conductor [1]
Optimize air gap profile (e.g. with heuristic methods [2])
Our proposition : We optimize the air gap profile using gradient descent methods.
Converge faster
More flexible parametrization
[1] R.A. Jensen and C.R. Sullivan, “Optimal core dimensional ratios for minimizing winding loss in high-frequency gapped-inductor windings,”
[2] D.I. Zaikin, S. Jonasen, and S.L. Mikkelsen, “An Air-Gap Shape Optimization for Fringing Field Eddy Current Loss Reductions in Power Magnetics,”
[3] https://info.triadmagnetics.com/blog/basics-of-inductors
[4] https://www.e-magnetica.pl/doku.php/proximity_effect
An inductor [3]
Fringing Effect [4]

## Slide 3: Outline
Introduction
Part I – Optimization Problem
Part II – Methodology
Part III – Optimization Results
Conclusion

## Slide 4: Part I – Optimization Problem

## Slide 5: Device and modeling
Device: A simplified inductor composed of a coil and a magnetic core
Goal: Minimizing the AC losses in the conductor keeping the inductance at mH.
Magneto-harmonic equation: ,
  where :
  ​ is magnetic vector potential out-of-plane component
  is real current density,
  and​ is the reluctivity which takes values :
Reference design
Reluctivity value () | Subdomain
 | Air region
 | Core region (ferrite)
with to model proximity effects at | Conductor region (copper)
 | Subdomain

## Slide 6: Objective and Constraint
AC Losses:
Inductance:
with (thickness) and (current, 200 turns).
The retained formulas are:

## Slide 7: Parametrization
Let be a parametrization of the air gap profile.
The following are dependent on :
the partition of the domain ,
the reluctivity ,
the magnetic potential solution of
AC Losses:
Inductance:
Then, the objective and constraint rewrites into :
Parametrized air gap

## Slide 8: Constrained Minimization Problem
Let be a parametrization of the air gap profile.
We aim to solve the following minimization problem to determine the optimal :

## Slide 9: Challenges and Solutions
Challenges : | Proposed solutions [1]:
Find good parametrizations of the air gap. | Control point vs Adaptative Mesh deformation.
Differentiate and with respect to … | Shape derivatives…
…and to the PDE constraint ! | …obtained by the adjoint method.
Find descent directions (How to find such that ?) that preserve the conductor domain. | Hilbertian extension-regularization.
Challenges : | Proposed solutions [1]:
 | Control point vs Adaptative Mesh deformation.
 | Shape derivatives…
…and to the PDE constraint ! | …obtained by the adjoint method.
 | Hilbertian extension-regularization.
We are using a handwritten augmented Lagrangian algorithm to solve this constrained optimization problem.
[1] G. Allaire, C. Dapogny, and F. Jouve, “Shape and topology optimization,” in Handbook of Numerical Analysis

## Slide 10: Part II - Methodology

## Slide 11: Two Choices for the Parametrization h
Parametric Shape Optimization using Control points
Geometric Shape Optimization by mesh deformation
Geometric Shape Optimization
by adaptative mesh deformation
using MMG [1]
[1] https://www.mmgtools.org/

## Slide 12: Shape derivatives
Shape derivative derivative of a functional w.r.t. the deformation of a domain
Considering:
  A bounded Lipschitz domain
  “Small and regular enough” deformation fields
  A real-value function of the domain
We define the deformed domain with respect to
The shape derivative of is the derivative of at :
We are searching a that is a descent direction:
Two approaches:
In our “control points” approach, is defined on the control points
In our “adaptative mesh deformation” approach, is defined on the mesh nodes.
Deformed domain

## Slide 13: Example of a Shape Derivative
For example, if we take a function ,
its shape derivative is:
This is the Reynolds transports theorem!
Finding a descent direction is obvious! For example:
Minimization of the integral.
The deformation makes
shrink in the (red) region where ,
and expend in the (blue) region where

## Slide 14: Shape Derivatives of Losses & Inductance
Recalling the formulas for the AC losses and the inductance :
  Losses :
  Inductance :
We introduce and the adjoint states given by the adjoint equations :
where the right-hand members are complex Fréchet-derivatives of real functions.
We compute the shape derivatives using the adjoint method and obtain :
with the real matrix
Those derivative formulas don’t directly reveal the descent directions; we need another step.

## Slide 15: Hilbertian Extension-Regularization
The “Hilbertian extension-regularization” technique consists in solving a Lax-Milgram-type equation of the form:
where :
is any subspace of (with wisely defined Dirichlet conditions),
is any inner product of .
Then is a descent direction : .
This procedure yields a regularized descent direction
with a structure that can preserve the conductor's boundary.

## Slide 16: Unregularized the Deformation Field
With a deformation field coming from:
,
Norm of
Vector field
Deformed mesh

## Slide 17: Regularized Deformation Field
With a deformation field coming from:
,
with
Norm of
Vector field
Deformed mesh

## Slide 18: Control Points Flowchart
Start
,
Initialize the control points
Generate the mesh based on the ,
Solve the magneto-harmonic equation,
Compute cost
Convergence ?
End
Solve adjoint equations,
Compute shape derivative ,
Compute descent direction
Update the control points:
Yes
No

## Slide 19: Adaptative Mesh Deformation Flowchart
Start
Convergence ?
End
Solve adjoint equations,
Compute shape derivative ,
Compute descent direction
Move the mesh nodes:
Yes
No
?
Perform MMG remeshing
No
Yes
Initialize the mesh
Solve the magneto-harmonic equation,
Compute cost

## Slide 20: Control Points Flowchart
Fig. 14: Flowchart for the “control points” approach

## Slide 21: Adaptative Mesh Deformation Flowchart
Fig. 15: Flowchart for the “adaptative mesh deformation” approach

## Slide 22: Part III – Optimization Results

## Slide 23: Results
Control points optimization results
Adaptative mesh deformation results

## Slide 26: Results – Performance and Convergence
Optimization results
Adaptative mesh deformation convergence curves
Optimization Type | Iterations | P (W) | L (mH)
Reference | - | 13.16 | 1.00
Control points | 92 | 6.00 | 1.00
Adaptative mesh deformation | 277 | 3.76 | 1.00

## Slide 27: Conclusion
We used gradient-based optimizations of the air gap profile of an inductor to minimize AC losses.
We leverage classical techniques such as:
  Control points, mesh deformations, remeshing
  Shape derivates
  Adjoint method
  Hilbertian extension-regularization
  Perspective:
    Include magnetic saturation in the optimization
    Find better topology of the magnetic core
    Include iron losses

## Slide 28: Thank You!
Code available on zenodo

## Slide 29: Results

## Slide 30: Results – Control Points

## Slide 31: Results – Adaptative Mesh Deformation

## Slide 32: Shape derivative of
The change of variables allows to transport the integral onto the fixed reference domain :
Considering that:
is Fréchet differentiable at , expanding to
is Fréchet differentiable at , expanding to .
By the product rule, is Fréchet differentiable at , and its derivative is the volume form :
Alternatively, if is a bounded and Lipschitz domain, an integration by parts gives the surface form :
Structural theorem : Under mild assumptions, if on then = 0.
The derivation can be difficult for elaborate functions, particularly those constrained by PDEs.

## Slide 33: Adjoint Method of
We want to differentiate a (e.g., the magnetic energy ) with respect to , an arbitrary parametrization of the air gap profile. Here, is the current density, and is the magnetic potential.
We introduce two equations:
The state equation
The adjoint equation : where is the adjoint operator of .
Then, the sensitivities of with respect to p can be expressed as :
The scalar product shown above varies based on how , ​, and ​ are represented:
if they are in discretized form, it's an scalar product, reflecting a "discretize then optimize" approach,
if they are in variational form, it's an scalar product, reflecting an "optimize then discretize" approach.
Jean Céa’s method offers an elegant way to obtain this result.

## Slide 34: Adjoint Method of
The state equation can be expressed in two ways:
Discretized Form: A linear system where is the stiffness matrix and is the discretized current density vector:
Variational Form: Where is a linear operator and is a linear form:

## Slide 35: Glimpse of Jean Céa’s method 1/3
To find the derivative of with respect to , we introduce a lagrangian function:
A key observation is that for any . Applying the chain rule, we get:
The challenge here is that is difficult to define rigorously and compute.
Jean Céa’s proposal is to choose such that the second term vanishes.
This is achieved by finding a saddle point of .

## Slide 36: Glimpse of Jean Céa’s method 2/3
Recalling the lagrangian function we posed :
Canceling with respect to , we obtain :
which recovers our original state equation .
Canceling with respect to , we obtain
Using the definition of the adjoint operator , this restates to
which recovers our original adjoint equation .
Thus, a saddle point of is .

## Slide 37: Glimpse of Jean Céa’s method 3/3
Recalling the lagrangian function we posed :
At the saddle point we have:
Thus, the formula for sensitivities is :
Applying this approach to shape derivatives demands special care
and yields more intricate expressions.